## Slide 1: Digital Systems and Computer Architecture Session 3.1 Mouli Sankaran
FSM, Moore and Mealy Models
Module 3

## Slide 2: Session 3.1: Focus
Finite State Machine (FSM)
  Example: Turnstile
Types of Clocked Sequential Circuits
  Moore Model
  Mealy Model
  Example circuits

## Slide 3: Finite State Machine

## Slide 4: Example: Turnstile
Allows people to enter through only on one side. It can also have controlled access (coin) to let people in.

## Slide 5: Operation of Turnstile Operation Explained
Operation is modeled with a State Machine or State Diagram
Turnstile can be in one of these two states
  Locked
  Unlocked
Initially it is in a Locked condition
Dropping a coin changes the state of the machine from Locked to Unlocked
Inputs are:
1. Coin
2. Push

## Slide 6: Turnstile Operation Explained
In the unlocked state, when the cross bar is pushed
  One person can move in through the gate
  Turnstile changes back to Locked state
  The cross bar cannot be moved in the locked state even if it gets pushed
There by allowing only maximum one person to enter for every coin dropped

## Slide 7: Finite State Machine (FSM)
A Finite-State Machine (FSM) or Finite-state Automaton (FSA, plural: automata), finite automaton, or simply a state machine, is a mathematical model of computation.
It is an abstract machine that can be in exactly one of a finite number of states at any given time.
The FSM can change from one state to another in response to some external inputs; the change from one state to another is called a transition.
A FSM is defined by a list of its states, its initial state, and the conditions for each transition.

## Slide 8: FSM of Turnstile
List of states
  Locked
  Unlocked
Initial State: Locked
External Inputs: Coin and Push
Transitions:
  Locked to Unlocked (Condition: Dropping of coin)
  Unlocked to Locked (Condition: Pushing the bar)
Dark dot here
Shows the
Initial state

## Slide 9: a) Moore Model
In the Moore model, the output is a function of only the present state.
  Present states are in tern driven by the inputs

## Slide 10: b) Mealy Model
In the Mealy model, the output is a function of both the present state and the inputs.
A circuit may also have both types of outputs.
  i.e., both Mealy and Moore type of outputs

## Slide 11: Mealy and Moore Machines
These two models of sequential circuits are commonly referred to as a Finite State Machine, abbreviated FSM.
The Mealy model of a sequential circuit is referred to as a Mealy FSM or Mealy machine.
The Moore model is referred to as a Moore FSM or Moore machine.

## Slide 12: Session 3.1: Summary
Finite State Machine (FSM)
  Example: Turnstile
Types of Clocked Sequential Circuits
  Moore Model
  Mealy Model