## Slide 1: Digital Systems and Computer Architecture Session 3.2 Mouli Sankaran
Analysis of Clocked Sequential Circuits
Module 3

## Slide 2: Session 3.2: Focus
Types of Sequential Circuits
Analysis of Clocked Sequential Circuits
  Logic Diagram
  State equations
  State Table
  State Diagram
Example 1: Moore Machine
Example 2: Mealy Machine

## Slide 3: Example : State Diagram
The information available in a state table can be represented graphically in the form of a state diagram.
A state is represented by a circle, and the (clock-triggered) transitions between states are indicated by directed lines connecting the circles
  Along with inputs that trigger the transitions)
Note: Since output is same as the present state,
It is not shown separately in the state diagram

## Slide 4: Example : State Diagram
State Table
State Diagram
This circuit acts as a 0-detector by asserting its output when a 0 is detected in a stream of 1s

## Slide 5: Example 1.3: State Table
The time sequence of inputs, outputs, and flip-flop states can be enumerated in a state table
  Also called as a transition table
Next state for all possible combinations of present states and inputs are defined
Z
Z is an Odd function
Z = 1, when there are
odd number of inputs

## Slide 6: State Diagram Explained
The state diagram provides the same information as the state table and is obtained directly from the state table
The binary number inside each circle identifies the state of the flip-flops.
The directed lines are labelled with two binary numbers separated by a slash.
The input value during the present state is labelled first, and the number after the slash gives the output during the present state with the given input (shown in Example 2)
It is important to remember that the bit value listed for the output along the directed line occurs during the present state and with the indicated input
  It has nothing to do with the transition to the next state.

## Slide 7: Steps in the Analysis
Circuit/Logic Diagram
State Equations
State Table
State Diagram
2
State equation
3
State table
4
State diagram
1
Logic diagram

## Slide 8: Example : State Equations
Output equation:
Next state values:
Mealy Machine
A
B
A
B
X
Y
X
Y
2.1 Logic Diagram
More convenient form:
More convenient form:
=
=

## Slide 9: Example : State Table
State Equations
A
B
A
B
X
Y
Logic Diagram
State Table
=
=

## Slide 10: Problem 1: State Table and State Diagram
Give the state table and state diagram of the circuit below:
State table:
TB
TA
TA=
A + B
A’ + B
1
Flip-flop inputs:
Initial state is 00
TB =

## Slide 11: Session 3.2: Summary
Types of Sequential Circuits
Analysis of Clocked Sequential Circuits
  Logic Diagram
  State equations
  State Table
  State Diagram
Example 1: Moore Machine
Example 2: Mealy Machine